## Slide 1: NAO
Programming a humanoid robot

## Slide 2: Introducing NAO
But I'll let him introduce himself!
Notes: Play on NAO the presentation.crg Choregraphe project, make sure the translation in your language is present.

## Slide 3: Choregraphe Software
NAO Visual Programming
  Allows users of NAO to create and edit simple movements and interactive behaviors.
Demonstration

## Slide 4: NAO's Mission
Make NAO walk towards you and stop in front of you.
NAO asks you to give him the ball and asks you where to put the ball.
NAO looks around and finds the place you identified.
NAO goes there, and places the ball down.

## Slide 5: Preparation
Start Choregraphe
Create a new project
Load the Library: Devoxx4Kids.cbl
Place and configure boxes
  Set Speech Language
  Set Reco. Lang.
  Tactile Head
Connect the boxes to the starting point.

## Slide 6: Exercise 1
Make NAO walk towards you
  Infrared Sensor (Eyes)
  Sonar
  Eye Color
Create a new box in the root plane
  Change the Name: Walk to Person
  Change the Image: move.png
  Type: Flow Diagram

## Slide 7: Exercise 1 (continued)
In the new box Walk to Person
  Make NAO stand (Stand Up)
  Walk Tracker
    Green eyes when NAO finds you (Eye Leds)
    Red eyes when he doesn’t find you (Eye Leds)
  Use NAO’s sonar
    Detect an obstacle (you)
    Stop the Walk Tracker
Link the sensor on NAO’s head to the new box

## Slide 8: Exercise 2
Ask the ball
  Raise right arm and open the hand
  Make NAO speak
  Make him understand what you say
    NAO ask a question with 2 possible answers
  Lower the arm and close the hand

## Slide 9: Exercise 2 (continued)
Create a new box in this plane
  Change its name (up to you to choose)
  Type: Flow Diagram
Add 2 outputs
  Double-click on the new box
  Click on the (top right)
  Name for output 1 : Chair
  Name for output 2: Box

## Slide 10: Exercise 2 (continued)
Change the color of the eyes
Raise NAO’s right hand (librairy)
  Box : Raise Right Hand
Make NAO speak with the Say box
  NAO must ask for the ball

## Slide 11: Exercise 2 (continued)
NAO asks where he should place the ball
  Create a nex box
    Type : Flow Diagram
  Add a Choice box
    Edit the output of the box
      Rename the output answer into answer1
        Type : Number : 1
        Naturel : Punctual
      Add a second output : answer2
        Type : Number : 1
        Naturel : Punctual
    Double-click on the box to enter the question and the answers
  Make NAO repeat the answer you gave him

## Slide 12: Exercise 2 (continued)
NAO lower his arm and close his hand
  Go back to root plane.
  Add a Close Right Hand box
    Link both outputs to the box

## Slide 13: Exercise 3
NAO looks for the right place where to drop the ball
  Turns his head
  Looks for the right NAOMARK
  Says he found the right place
  Says he hasn’t find the right place

## Slide 14: Exercise 3 (continued)
Create a new box in the main place
  Change name : Research
  Type: Flow Diagram
Add 1 output
  Double-click on the new box
  Click the (top right corner)
  Name for the output : Found

## Slide 15: Exercise 3 (continued)
In the new box, add:
  A NAOMark box
  A Center Head box
  A Move Head Left box
  A Move Head Right box
  An IF box
  Two Say boxes
  Three Wait boxes (Change timeout to 4,000000)

## Slide 16: Exercise 3 (continued)
  Connect the starting input of Research box to:
    Center Head
    NAOMark
    A wait box
  Make NAO’s head turn from left (Move Head Left) to right (Move Head Right)
  Connect the NAOMark to the IF box
    Configure the IF box :
      Condition Operator : =
      Value to compare : 68

## Slide 17: Exercise 3 (continued)
  Conect the output output_then of the IF box to the Input :
    onStop of boxes Wait, Move Head Left, Move Head Right
    onStart of a Say box
      Use Say box to say that NAO has found a box to drop the ball
      Don’t forget to make NAO say he hasn’t find any box where to drop the ball. It’s up to you to find out how to do!
  Then get back to main plane and do the same thing for the chair (copy/paste + modifications).

## Slide 18: Exercise 4
NAO goes to the required place to drop the ball
  Walk to the box or the chair (NAOMARK)
  Sfoot sensorsenseurs des pieds to avoid collision with box or chair
  Drop the ball

## Slide 19: Exercise 4 (continued)
Create a new box in root plane:
  Edit name: Walk to NAOMark
  Type: Flow Diagram

## Slide 20: Exercise 4 (continued)
In the new box, add:
  A Mark Walk Tracker box
  A NAO facing Mark box
  A Bumpers box
  A Move To box
  A Say box
  2 Wait boxes (Change timeout to 0,500000)
  2 Eye LEDs boxes
  A Drop Ball Move Back and Sit box

## Slide 21: Exercise 4 (continued)
Connect the starting point of Walk to NAOMark box to the input of NAO facing Mark
Connect the output of NAO facing Mark àto the input onStart of:
  Bumpers :
    NAO must walk 2 steps backward
    Stop all other boxes
    NAO must say he found the place « Im in! »
  Mark Walk Tracker
    Eyes turn to blue if NAOMark is no longer detected
      Output: onLost connected to Input onStop
      NAO take a step
      NAO must say he has arrived « Im in »
    Green eyes if NAOMark is detected

## Slide 22: Exercise 4 (continued)
In the root plane, add the Drop Ball Move Back and Sit box and connect it to the Walk to NAOMark box